STEERING POST PIVOT ADAPTER

Thank you for purchasing the RSI Steering Post Pivot Adapter.

This adapter converts your flat style steering post to a pivot style steering post.

- Remove stock handlebar clamps and handlebars from the steering post.

- Mount the adapter to the steering post with the supplied bolts and lock washers.  A small amount of thread locker is recommended.  The bolts install from the bottom of the steering post flat plate and thread into the adaptor.

Note:  Some models will require you to slightly drill out the steering post bolt holes to allow adaptor bolts to go through.  Slight filing on the holes may be required to clean up the holes for proper alignment.

- Tighten the mounting bolts evenly.

- Install risers and handlebars making sure snowmobile throttle and steering is functioning properly.

- Check bolt tightness after each ride.

Disclaimer:

RSI  assumes no liability for mechanical damage, engine damage, personal injury or crash damage of any kind do to improper installation or use of this product.  The owner / operator of the snowmobile assumes all liability when using this product on their snowmobile.© Copyright 2017-2019' All Rights reserved.